Product Description

MDC interface 100G SR4 optical module adopts QSFP package and supports MDC connector cables. 4 groups of MDC optical interfaces are used for connection, and a total of 8 optical fibers are used for parallel transmission. The MDC connector is a duplex connector designed to provide efficient, high-density fiber optic connections.

100G QSFP28 transceiver modules are designed for use in 100 Gigabit Ethernet links over multimode fiber. They are compliant with the QSFP28 MSA and IEEE 802.3bm 100GBASE-SR4 and CAUI-4. Digital diagnostics functions are available via the I2C interface, as specified by the QSFP28 MSA. The transceiver is RoHS-6 compliant per Directive 2011/65/EU.

Electrical Characteristics (EOL, TOP = 0 to 70C, VCC = 3.135 to 3.465 Volts)

| Parameter | Symbol | Min. | Typical | Max. | Unit | Note |
| --- | --- | --- | --- | --- | --- | --- |
| Supply Voltage | Vcc | 3.135 |  | 3.465 | V |  |
| Supply Current | Icc |  |  | 800 | mA |  |
| Module total power | P |  |  | 2.5 | W |  |
| Transmitter Section: |
| Signaling rate per lane |  | 25.78125 ± 100ppm | Gb/s |  |
| Differential pk-pk input voltage tolerance | Vin,pp,diff |  |  | 900 | mV |  |
| Single-ended voltage tolerance | Vin,pp | -0.35 |  | +3.3 | V |  |
| Module stress input test |  | Per Section 83E.3.4.1, IEEE 802.3bm | V |  |
| Receiver Section: |
| Signaling rate per lane |  | 25.78125 ± 100ppm | V |  |
| Differential data output swing | Vout,pp | 100 |  | 400 | mVpp |  |
|  |  | 300 |  | 600 |  |  |
|  |  | 400 | 600 | 800 |  |  |
|  |  | 600 |  | 1200 |  |  |
| Eye width |  | 0.57 |  |  | UI |  |
| Eye height, differential |  | 228 |  |  | mV |  |
| Vertical eye closure | VEC | 5.5 |  |  | dB |  |
| Transition time (20% to 80%) | tr, tf | 12 |  |  | ps |  |

Optical Characteristics (EOL, TOP = 0 to 70C, VCC = 3.135 to 3.465 Volts)

| Parameter | Symbol | Min. | Typical | Max. | Unit | Note |
| --- | --- | --- | --- | --- | --- | --- |
| Transmitter Section: |
| Center Wavelength | λt | 840 | 850 | 860 | nm |  |
| RMS spectral width | △λ |  |  | 0.6 | nm |  |
| Average Optical Power per Lane | TXPx | -8.4 |  | 2.4 | dBm |  |
| Optical Power OMA per Lane | TxOMA | -6.4 |  | 3 | dBm |  |
| Launch Power [OMA] minus TDEC per Lane | P-TDEC | -7.3 |  |  | dBm |  |
| TDEC per Lane | TDEC |  |  | 4.3 | dBm |  |
| Optical Extinction Ratio | ER | 2 |  |  | dB |  |
| Optical Return Loss Tolerance | ORL |  |  | 12 | dB |  |
| Encircled Flux | FLX | >86% at 19 um <30% at 4.5 um | dB |  |
| Average Launch Power of OFF Transmitter, per Lane |  |  |  | -30 | dBm |  |
| Transmitter Eye mask definition {X1, X2, X3, Y1, Y2, Y3} |  | {0.3,0.38,0.45,0.35,0.41,0.5} |  | 2 |
| Receiver Section: |
| Signaling Speed per Lane |  | 25.78125 ± 100ppm | Gb/s | 3 |
| Center Wavelength | λr | 840 |  | 860 | nm |  |
| Damage Threshold | DT | 3.4 |  |  | dBm |  |
| Average Lane | Receive | Power | per | RXPx | -10.3 |  | 2.4 | dBm |  |
| Receive Power (OMA) per Lane | RxOMA |  |  | 3 | dBm |  |
| Receiver Reflectance | Rfl |  |  | -12 | dB |  |
| Stressed Sensitivity (OMA) | SRS |  |  | -5.2 | dBm | 4 |
| Stressed Conditions: |  |  |  |  |  |  |
| Stressed Eye Closure | SEC | 4.3 | dB |  |
| Stressed Eye J2 Jitter | J2 | 0.39 | UI |  |
| Stressed Eye J4 Jitter | J4 | 0.53 | UI |  |
| OMA of each aggressor lane |  | 3 | dBm |  |
| Stressed Receiver Eye Mask Definition {X1, X2, X3, Y1, Y2,Y3} |  | {0.28,0.5,0.5,0.33,0.33,0.4} |  | 5 |
| Los De-Assert | LOSD |  |  | -13 | dBm |  |
| Los Assert | LOSA | -30 |  |  | dBm |  |
| Los Hysteresis | LOSH | 0.5 | 2 |  | dB |  |

Note:

  - Transmitter consists of 4 lasers operating at a maximum speed of 25.78125Gb/s ±100ppm each.

  - Hit Ratio 1.5 x 10-3 hits/sample.

  - Receiver consists of 4 photo detectors operating at a maximum speed of 25.78125Gb/s±100ppm each.

  - Minimum value is informative only and not the principal indicator of signal strength.

  - Hit Ratio 5 x 10-5 hits/sample

# General Specifications

| Parameter | Symbol | Min. | Typical | Max. | Unit |
| --- | --- | --- | --- | --- | --- |
| Bit Rate (all wavelengths combined) | BR |  |  | 103.1 | Gb/s |
| Bit Error Ratio (pre-FEC) | BER |  |  | 5x10-5 |  |
| Maximum Supported Distances |
| Fiber Type |  |  |  |  |  |
| OM3 MMF | Lmax1 |  |  | 70 | m |
| OM4 MMF | Lmax2 |  |  | 100 | m |

# Pin Assignment:

Order Guide

| No. | Product Code | Product Description |
| --- | --- | --- |
| 1 | 9950107 | 100G SR4 transceiver w/MDC optical conn interface |

Product Specifications

About ADTEK

Established in 2007, Shenzhen ADTEK Technology Co.,Ltd, located in Shenzhen, is a national high-tech enterprise integrating R & D, production, operation and service.

The company focuses on providing optical fiber and copper cable connection products for global customers, and provides one-stop fiber optic cabling system and network cabling solutions for domestic and foreign operators, telecom main equipment suppliers and system integrators.

Our main products cover high-density data centers, 5G fronthaul, OBO onboard connections, FTTX etc. Based on the purpose of "Quality is everything", our products have passed CE, RoHS, UL, FCC and other certifications to ensure the reliability and stability of each product and provide excellent products for our customers.

# Text boxes

100G SR4 QSFP28 Optical Transceiver

Product Specifications

www.adtekdata.com

100G SR4 QSFP28 Optical Transceiver（MDC Interface）

Product Features

· Hot Pluggable QSFP28 form factor

· Supports 103.1Gb/s aggregate bit rate

· Maximum link length of 100m on OM4 Multimode Fiber (MMF)

· MDC interface

· Single 3.3V power supply

· Typical Power dissipation <1.8W

· 4x25Gb/s 850mm VCSEL-based transmitter

· 4x25G electrical interface

· I2C management interface

· Commercial operating case temperature range: 0°C to 70°C

Data Center Cabinet

Fiber Optic Patch Cord

Fiber Optic Patch Panel

Copper Cable Connection Products

WDM

AOC

More Products: https://www.adtekdata.com

6

www.adtekdata.com

SHENZHEN ADTEK TECHNOLOGY CO., LIMITED

Tel: 0086-0755-83545255

E-mail: marketing@adtek-fiber.com

Address: 16/F, Building 1, Nanshan iPark Chongwen, No.3370 Liuxian Avenue, Nanshan District, Shenzhen, China